## Slide 1: Dr. Corey J. Bishop Assistant Professor of Biomedical Engineering Principal Investigator of the Pharmacoengineering Laboratory: pharmacoengineering.com Dwight Look College of Engineering Texas A&M University Emerging Technologies Building Room 5016 College Station, TX 77843 cbishop@tamu.edu
BMOLE 452-689 – Transport
Chapter 10. Mass Transport and Biochemical Interactions
Text Book: Transport Phenomena in Biological Systems
Authors: Truskey, Yuan, Katz
Focus on what is presented in class and problems…

## Slide 2: Reaction mechanisms
Generally, Rates = constant * (reactants or products)
If disappearing or appearing dictates the sign
Reaction orders of individual reactants or products (a +b +c) = overall reaction order
Is k actually a constant?
What affects k the most?
Arrhenius equation
Ea = energy of activation (Joules)
A = a constant for each chemical reaction defining the frequency of collisions in correct orientation
Units of exponent?
Units of k?
How do you know the units of k?

## Slide 3: An equation for the general half-life of any nth order differential equation

## Slide 4
Examples
For n=1
Because:
We can say that:

## Slide 5: Matrix Math for Chemical Reactions
Chapter 2
Multi-Step Reactions: The methods for Analytical Solving the Direct Problem
The following slides are based on this chapter cited below…
https://link.springer.com/chapter/10.1007%2F978-3-7091-0531-3_2#page-1

## Slide 6
Short-hand

## Slide 7: Another example:

## Slide 8: How to solve concentrations as a function of time using eigenvectors and eigenvalues
Av- λv=0
v(A- λ?)=0… not mathematically possible
v(A- λI)=0
Solve for λ and then using Av= λv solve for eigenvectors
Remember they are scalable and translatable and usually they are normalized to have a magnitude of 1 and translated to the origin

## Slide 9
Multiple by dt
Separate variables properly
integrate
Matrix diagonalization…
Matrix diagonalization
A = PDP-1
P = eigenvector matrix
D = diagonalization of
Eigenvalues via Identity Matrix
i.e.,
k= xΛx-1
So

## Slide 10: Given: K = [1 -1; 2 4]; what is D and V
Caclulate compartments CA(t) and CB(t) using:
Be able to get to this end stage from knowing a compartmental scheme… i.e.,
I want you to be able to know every step for a simple 2x2 matrix (use numbers instead of ks, however) to get to C(t).
I do want you to solve the rate matrix using a scheme such as the one shown…
You should know though that to make sense there should be rate constants (and/or numbers) in the matrix K but for
Simplicity to show the math process K is a function of numbers only here

## Slide 11
A = randn(3,3);
[V,D]=eig(A); V = 3x3 and D = a diagonal 3x3 with eigenvalues on diag.
A*V = V*D and A*V(:,1)=V(:,1)*D(1,1)
If A = symmetric then there are 3 eigenvalues (not necessarily distinct) and 3 orthogonal eigenvectors…
How to from A calculate eigenvalues and eigenvectors.
To do manually:
Ex: from A= [3 0 0; 0 3 0; 0 0 3] or any A… making it simple for example…
A-lambda*I = 0; solve for lambdas; each root is a lambda i.e., (λ-3)*(λ-3)*(λ-3)=0
Then solve for V1 by A*V(:,1)=V(:,1)*D(1,1)
Then solve for V2 by A*V(:,2)=V(:,2)*D(2,2)
Then solve for V3 by A*V(:,3)=V(:,3)*D(3,3);
Now let’s convince ourselves:

## Slide 12: Is this equal to exp(V*D*m*inv(D))Co in matlab? Is this equal to Coexp(Kt)? Matlab won’t let you use symbolic math with t; reserved for other things… MatLab has a hard time simplifying: V*exp(D*t)*inv(V)*Co

## Slide 13: Clc
k*C = dC/dt
k*dt = 1/C dC
exp(kt)+constant = C(t)
exp(kt)*constant=C(t)
syms k1, k2, k3, k4
How do you solve for V and D manually from K?

## Slide 14
Another example:
Multiple by dt
Separate variables properly
integrate

## Slide 15
Only solve for for fA and fB

## Slide 16: Pharmacokinetics (PK) and Pharmacodynamics (PD)
Difference?

## Slide 17: Pharmacokinetics (PK) and Pharmacodynamics (PD)
Difference?

## Slide 18: Common variables for PK/PD
Cp=plasma concentration of drug
DB, D0=drug amount in body, initial drug concentration
Cl, ClR, ClH, ClT , ClNR=clearance, renal clearance, hepatic, total body, non-renal
VD= volume distribution of drug
R = rate of infusion into systemic circulation
k, km, ke, ka=degradation rate, metabolism rate, excretion rate, absorption rate
AUC = area under the curve (Cp(t))
F= bioavailability
Du= drug amount in urine
Ab = absorption

## Slide 19: PK
Volume of dist. (Vd)?
  Do/Cp
ko
k
  Cl/Vd
    krenal Clrenal/Vd
  kmetabolism+krenal+khepatic
ClHepatic, renal, total
  Clearances also sum
    Cltotal = Clrenal + Clnon-renal

## Slide 20: Cp as a function of clearance, volume of distribution, and initial drug amount

## Slide 21: Vd as a function of k, the initial drug amount, and the AUC (Cp vs t)
Including Bioavailability: F*Do

## Slide 22: Kidneys

## Slide 23: Endeavoring to use easy-access variables to characterize clearance for a patient (to cater drug regimen) or drug for healthy patients
Sub-portion:
Total:

## Slide 24: A useful, non-invasive way to quantify Clrenal

## Slide 25: GI or Dermal
How many exponentials are describing this Cp(t) profile? How many compartments are here?
Is this for dermal or GI delivery? How would this be modified if it were IV?
How does the first-pass effect come into play?
ON BOARD LAPLACE EXAMPLE…

## Slide 26: Infusion pumps

## Slide 27: Example of quantifying kinetics from my own research

## Slide 28
http://www.sciencedirect.com/science/article/pii/S1742706116301325

## Slide 29
http://www.sciencedirect.com/science/article/pii/S1742706116301325

## Slide 30
Use: kcell, kne, kni, kbd equal to 7.5e-4, 0.72, 1.1, and 1.8 hr-1
kdeg1 and kdeg2 equal to 0.62
And 0.084 hr-1
Where A+B at t=2 hours is total plasmid #
in cell. i.e., 6500 plasmids
http://www.sciencedirect.com/science/article/pii/S1742706116301325
P = plasmid # (note that volume is not taken into account); simply # of plasmids in a given compartment at any given time t.
Why 2 degradation rates of plasmids (polyplex context)?

## Slide 31
Be able to
do this
Why a Heaviside step function (HSSF)?
Use: kcell, kne, kni, kbd equal to 7.5e-4, 0.72, 1.1, and 1.8 hr-1
kdeg1 and kdeg2 equal to 0.62
And 0.084 hr-1
Where A+B at t=2 hours is total plasmid #
in cell. i.e., 6500 plasmids
http://www.sciencedirect.com/science/article/pii/S1742706116301325
What is the rate limiting step? Why is it what it is and not perhaps the expected
nuclear uptake step?
P = plasmid # (note that volume is not taken into account); simply # of plasmids in a given compartment at any given time t.
Why 2 degradation rates of plasmids (polyplex context)?

## Slide 32
Be able to
do this
Why a Heaviside step function (HSSF)?
Apply Laplace to solve…
How would you do this?
How would you deal with the HSSF without
Taking the laplace of the HSSF.
Be able to
do this
Use: kcell, kne, kni, kbd equal to 7.5e-4, 0.72, 1.1, and 1.8 hr-1
kdeg1 and kdeg2 equal to 0.62
And 0.084 hr-1
Where A+B at t=2 hours is total plasmid #
in cell. i.e., 6500 plasmids
http://www.sciencedirect.com/science/article/pii/S1742706116301325
What is the rate limiting step? Why is it what it is and not perhaps the expected
nuclear uptake step?
P = plasmid # (note that volume is not taken into account); simply # of plasmids in a given compartment at any given time t.
Why 2 degradation rates of plasmids (polyplex context)?

## Slide 33
http://www.sciencedirect.com/science/article/pii/S1742706116301325